## Slide 1: Boolean Algebra

## Slide 2: Introduction
The principle behind Boolean Algebra is that the answers to its equations are either True or False.
Where Digit 1 or letter T is used to represent a True solution and the Digit 0 or letter F for a False solution.

## Slide 3: Switching circuits and Boolean Algebra
The logic of Boolean Algebra was used to analyze switching circuits by a mathematician Claude Shannon in 1938 at Bell Laboratories.
A switch circuit is composed of interconnected switches. A switch can either be closed (Hence electrical current passes through it, as shown in Fig-1) and when the switch is open the (current cannot pass through it, as shown in Fig-2).
Switch Closed
Switch Open
Fig - 1
Fig - 2

## Slide 4: AND/OR Operations
Let us consider a situation as shown in Fig A
Here we have two switches S1 and S2 connected in series with a battery and electric bulb B.
Lets determine the flow of current with regard to the following switches.
Battery
Bulb B
Current Flow
Switch S1
Switch S2
Fig A
Switch connected in series

## Slide 5: And Operation
Now as the current flows through the switches S1 and S2, lets see what happens.
CASE 1) Where S1 = Open and S2 = Open
CASE 2) When S1 = Open and S2 = Closed
CASE 3) When S1 = Closed and S2 = Open
CASE 4) When S1 = Closed and S2 = Closed
1 = Yes (True) and 0 = No (False)
Result of the above cases
S1
S2
Current Flow - B
No
No
No
No
Yes
No
Yes
No
No
Yes
Yes
Yes
Simplified Table
S1
S2
Current Flow B
0
0
0
0
1
0
1
0
0
1
1
1

## Slide 6: Truth Table for AND
In symbolic logic, the AND operator is known as : logical AND or logical product. An alternative term for logical AND is conjugation.
A truth table is nothing but the combination of all possible inputs and their effect on the output(s) of a switching circuit.
A
B
Output
0
0
1
1
0
1
0
1
0
0
0
1
Truth Table for AND
B = S1 AND S2

## Slide 7: OR Operation
Let us consider another switching circuit, here the switches are connected in parallel.
Battery
Bulb B
Current Flow
Switch S1
Switch S2

## Slide 8: Truth Table for OR
Lets see how the current flows and what is the output. So we have B = S1 OR S2
S1
S2
Current
No
No
Yes
Yes
No
Yes
No
Yes
No
Yes
Yes
Yes
Flow of current
A
B
OUT
0
0
1
1
0
1
0
1
0
1
1
1
Truth Table for OR
Switch 0 = Open
1 = Closed
Bulb 0 = No current
1 = Current Flow
Hence OR connective is termed as logical OR or logical sum. An alternative term
for Logical OR is Disjunction.

## Slide 9: NOT Operation
Let us take a switching circuit where S is connected in this circuit in such a way that if it is Open then the current flows through the bulb and vise-versa.
B= Not S
In symbolic logic the NOT operator is termed as logical not or logical negative or inverse.
Battery
Bulb B
Switch S
S
B
0
1
1
0
Table

## Slide 10: Boolean Variables and Experssions
A boolean variable can have only two values: true or false, 1 or 0, closed switch or open switch, etc.
Therefore boolean variable are binary or two valued. A boolean variable is also known as literal.

## Slide 11: We may write a simple boolean expression as below.
X=A AND B OR (NOT C)
Where X is the resulting value.
A, B , C are Variables.
In an expression logical operators are represented as below:
AND = + (sum)
OR = . (product)
NOT = ’ (inverse)
Thus the boolean expression will be as follows:
X=A+B.C’

## Slide 12: Rules while solving the Complex Boolean expressions
There would be confusion while evaluating complex Boolean expression, as to which Boolean operator should be applied first.
Lets take the following example:
p = a + b’ . c + d’ + b’ . d
This problem can be solved by following the order of precedence for the operators given
RULE set :- 1
NOT (This operator has highest priority)
AND
OR (This operator has the lowest Priority)
RULE set : - 2
Evaluate from Left to Right
Evaluate the expressions in parentheses
Perform all the NOT operators first
Then Perform all AND operators
At the end Perform all the OR operators

## Slide 13: Solving Complex Expressions
Lets Solve the following expression using the rules discussed:
a + b’ . c + d’ + b’ . d
Part 1
Part 2
Part 3
Part 4
Part 5
So we solve the Part 1, Part 2, Part 3,
Part4 and then part 5
a + b’ . ( c + d’ ) + b’ . d
Hence p =
a + b’ . ( c + d’ ) + b’ . d

## Slide 14
Postulates
Postulates and Theorems of Boolean Algebra
Assume A, B, and C are logical states that can have the values 0 (false) and 1 (true). "+" means OR, "·" means AND, and NOT[A] means NOT A.
(1) | A + 0 = A | A · 1 = A | identity
(2) | A + A’ = 1 | A · A’ = 0 | complement
(3) | A + B = B + A | A · B = B · A | commutative law
(4) | A + (B + C) = (A + B) + C | A · (B · C) = (A · B) · C | associative law
(5) | A + (B · C) = (A + B) · (A + C) | A · (B + C) = (A · B) + (A · C) | distributive law
Theorems
(6) | A + A = A | A · A = A | IDEMPOTENT LAW
(7) | A + 1 = 1 | A · 0 = 0 | Dominance of 0 and 1
(8) | A + (A · B) = A | A · ( A + B) = A | Absorption law
(9) | A + (A’ · B) = A + B | A · (A’ + B) = A · B | Involuted Theorem
(10) | (A · B) + (A’ · C) + (B · C) = (A · B) + (A’ · C) | A · (B + C) = (A · B) + (A · C) | 
(11) | [A + B]’ = A’ . B’ | [A · B]’ = A’ + B’ | de Morgan's theorem

## Slide 15: Theorems of Boolean Algebra
The following Theorems are very important for the manipulation of Boolean expressions.
THEOREM 1:- The Boolean algebra is IDEMPOTENT
a + a = a
a . a = a
The above stated law is known as Idempotent laws.
THEOREM 2:- The Boolean Algebra allows the dominance of 0 and 1 such that a + 1 = 1
a . 0 = 0
THEOREM 3:- The Boolean Algebra is ABSORPTIVE
a + (a . b) = a
a . (a + b) = a
The above stated law is known as absorption laws.
THEOREM 4:- The Boolean algebra is INVOLUTED
(a’)’ = a

## Slide 16: De Morgan’s Theorem
De Morgan, a friend of Boole, worked extensively in logic and mathematics, he contributed the following two very important theorems:-
THEOREM 5:- It says that “ The complement of a sum equals the product of the complements”.
(a + b)’ = a’ . b’
THEOREM 6:- This Theorem says that “The complement of the product equals the sum of the complements”.
(a . b)’ = a’ + b’
The following Theorems can be deduced from the basic postulates of the Boolean Algebra.
1. a + (a’ . b) = a + b
a . b + a’ . c + b . c = a b + a’ c
(a + b) . (a + c) = a + b c