## Slide 1: Number Systems

## Slide 2: Different types of number systems
Decimal numbers(0-9)
Binary numbers(represented in combinations of 1s and 0s)
Hexadecimal numbers(0-9 A-F)

## Slide 3: Converting Binary to Decimal
Take each 1s position.
Minus 1 from that.
Represent each 1 = 2(position-1)
At the end add all the 1s representation.
e.g. 10001001 will be calculated as:
27+23+20
128+8+1 so the answer is : 137

## Slide 4: Converting from Decimal to Binary
Go on dividing the number by 2, the remainder in reverse is your binary digit.
2 125 1
2 62 0
2 31 1
2 15 1
2 7 1
2 3 1
2 1 1
1 0

## Slide 5: Table of Binary, Decimal & Hexadecimal
Decimal | Binary | Hexadecimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 6: Conversion of Fractional Decimal to Fractional Binary
Multiply the fractional decimal by 2
The result will be a fraction part and a decimal part
Write the integer part in a column
The fraction part becomes the new fraction
Continue the process till the fraction part is 0
The integer part column is your fractional binary digit.

## Slide 7: Example of fractional decimal to fractional binary
Fractional Decimal Number | Operation | Product | Fractional part of product | Integer part of product
0.625 | Multiply by 2 | 1.250 | .250 | 1
0.250 | -do- | 0.500 | .500 | 0
0.500 | -do- | 1.000 | 0 | 1
Hence the original number that was 0.625 was converted into a fractional binary number 0.101
The result should be written as (0.625)10 = (0.101)2

## Slide 8: Conversion of fractional binary to fractional decimal
Write out binary number as negative powers of 2
Convert each power of two into its decimal equivalent
Add these to give the decimal number

## Slide 9: Example
Original number : 0.1011

## Slide 10: Octal Number Notation
Octal is 0-7
Converting binary to octal is easy:
e.g. 11001 can be grouped in two parts
011 001
Replace each group with its octal equivalent
That is 3 and 1 we get 31 as the answer
Hence we write it as :
(11001)2 = (31)8

## Slide 11: Don’t forget to go through the data representation chapter in your books